## Slide 1: The Study of the Deactivation of CeO2-based Catalysts in Ethanol Steam Reforming using Raman Spectroscopy
Final Project
Mohammed Sifat

## Slide 2: Research Background
CeO2-based catalysts have been studied for their high oxygen storage capacity (OSC) and versatile role as a catalyst support.
Inclusion of transition metals (TM) on surface (Ni, Co) and promoters (K, Zr, Y) in the support for increased reactant selectivity and stability.
Ethanol Steam Reforming (ESR) is an industrial reaction investigated as a renewable means of H2 production for energy use.
Deactivation in the form of carbon deposition (coking) can be studied using structural characterization techniques like Raman Spectroscopy.
[1]
[2]
[1] S. Ogo and Y. Sekine. Fuel Processing Technology 199 (2020) 106
[2] C. Montero et al. Ind. Eng. Chem. Res. 2019, 58, 14736−14751

## Slide 3: Overview: Raman Spectroscopy
Raman spectroscopy is used to study the interaction of monochromatic (laser) light with different chemical structures.
Raman spectra can be used to determine the structure and bond behavior of various crystalline compounds, especially material with a strong Raman signal like CeO2 .
Material can be tested ex-situ (exposed to ambient environment) or in-situ (under the flow of fluidized reactants) which both impact the quality (signal-to-noise ratio) of the spectra.
[3]
[3]
[3] Raman Spectroscopy - FAQ. Agilent - Chemical Analysis, Life Sciences, and Diagnostics. (n.d.). https://www.agilent.com/en/support/molecular-spectroscopy/raman-spectroscopy/what-is-raman-spectroscopy-faq-guide

## Slide 4: Objectives of Project
Read, normalize and plot n number of Raman spectrum files
Save normalized and shifted data to a .csv for more complicated data processing in programs like Origin
Fit and integrate peaks of interest in a given Raman spectrum

## Slide 5: Example of File Contents:
Data Input:
Files are already “clean” (i.e., no need to remove unnecessary information) from Raman system used
Can be a combination of spent (following reaction) and fresh (before reaction) catalysts
Will need to refer to file for exact Raman shift values during user input stage.

## Slide 6: Modules used:
Script 1:
Normalization, plotting & data storage:
Script 2:
Curve fitting, plotting & peak integration:

## Slide 7: User inputs:
Script 1:
Script 2:
File handling:

## Slide 8: Script 1: Normalization
Normalization Sequence:
1. Specify the reference normalization peak (norm) by indexing the respective location in list x axis
2. After locating, get corresponding y value from each spectrum
3. Subtract a corresponding baseline y value (ex. y value at ~800 cm-1) from y value located in step prior
4. Compare each new resulting difference for each spectrum and select largest value to set as reference
5. Divide the norm by each delta and store each factor to a variable
6. Multiply the each of the spectrums' y axis data by their corresponding factor
7. Resulting list is new y axis for each new normalized spectrum
8. Code can then be replicated depending on the varying amounts of spectra as needed.
tl;dr: The amplitude of the spectrum with the most intense characteristic peak is used to adjust every other spectrum by a relative factor.

## Slide 9: Script 1: Plotting and Storage

## Slide 10: Script 2: Curve Fitting and Peak Integration
AD/AG = 1.39
D band:
G band:
Parameters:

## Slide 11
Conclusions and Future Work
Conclusions:
  Based only on the spent catalysts, the addition of a promoter (Catalyst 2) to the Ni/CeZrO2 catalyst (Catalyst 4) seemed to reduce carbon (coke) deposition.
  Catalyst 2 performed better in terms of catalyst lifespan since it had lower deposits of carbon shown by the normalized data.
    This is shown by the relatively smaller peaks in spectrum 2 than spectrum 4 in the ~1250-1750 cm-1 range (i.e., lower total AD&G area).
  AD/AG is comparable (1.29 vs. 1.39) for Catalyst 4 than Catalyst 2, indicating a similar rate of coke propagation between each catalyst.
  A right Raman shift of spent samples (F2g peak) compared to fresh indicates shortening of bond length following reaction.
Future Work:
  Try to optimize fit further
  Automate entire process in a single script
  Fit multiple peaks using more complicated Gaussian-Lorentzian functions
  Elemental composition as well as electronic state information (EDX, XAS, XPS) will be needed to determine location and incorporation of promoter.
F2g